Irrigation Water Requirement

The following data applies to the growth of a vegetable crop. Complete the table.

| Week | P.E.T. (mm) | Kc | A.C.E. (mm) | Rainfall (mm) | Irrigation water Required (mm) |
| --- | --- | --- | --- | --- | --- |
| 1 | 133.00 | 0.40 | 53.20 | 60.00 | -6.80 |
| 2 | 125.00 | 0.63 | 78.75 | 33.00 | 45.75 |
| 3 | 150.00 | 0.70 | 105.00 | 25.00 | 80.00 |
| 4 | 185.00 | 0.75 | 138.75 | 28.00 | 110.75 |
| 5 | 140.00 | 0.80 | 112.00 | 26.00 | 86.00 |
| 6 | 195.00 | 0.85 | 165.75 | 41.00 | 124.75 |
| 7 | 200.00 | 0.85 | 170.00 | 58.00 | 112.00 |
| 8 | 170.00 | 0.81 | 137.70 | 161.00 | 0.00 |
| 9 | 200.00 | 0.75 | 150.00 | 62.00 | 88.00 |
| 10 | 185.00 | 0.65 | 120.25 | 53.00 | 67.25 |
| 11 | 150.00 | 0.55 | 82.50 | 75.00 | 7.50 |
| 12 | 195.00 | 0.45 | 87.75 | 41.00 | 46.75 |
| Total Depth of Water Required = |  |

ACE = PET x Kc

Irrigation water required *= ACE - Rainfall

* : If rainfall exceeds ACE, no irrigation water is required

Irrigation Efficiency

A stream of 7 ft3/s was diverted from a river and 3.8 ft3/s was delivered to a field. An area of 2 acres (1 acre = 43,560 ft2) was irrigated for 8 hours. Some of the irrigation water left the plot as runoff at an average rate of 0.8 ft3/s for 8 hours. At the end of the irrigation period 6 inches of water were added to the root zone. A total of 9 inches of water were required in the root zone at the beginning of irrigation. Determine

i) Water - Conveyance Efficiency

ii) Water - Application Efficiency

iii) Water - Storage Efficiency

Distribution Efficiency Problem

After the operation of a single sprinkler, the following application depths were measured at 5 ft intervals from the sprinkler.

| Distance from sprinkler (ft) | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Application Depth (cm) | 18 | 15 | 10 | 7 | 5 | 3 | 2 | 0 |

Determine the distribution efficiency for two such sprinklers spaced

a) 20 ft apart, and b) 25 ft apart. Which of the two spacing gives the more uniform coverage.