Runoff Practice Problems:

Determine the runoff volume for a 3 inch rainfall in Decatur, Illinois for the following watershed.

Land Use			Percent of Area		HSG		CN

Residential (1/4 acre lots)			45			   B

Residential (1/4 acre lots)			25			   C

Commercial					20			   B

Open	 Space					10			   B

| Land Use | Percent of Area | HSG | CN | % of Area x CN/100 |
| --- | --- | --- | --- | --- |
| Residential (1/4 acre lots) | 45 | B | 75 | 33.75 |
| Residential (1/4 acre lots) | 25 | C | 83 | 20.75 |
| Commercial | 20 | B | 69 | 13.8 |
| Open Space | 10 | B | 82 | 8.2 |
| Area weighted Curve Number | 76.5 |

Graphical Solution

Arithmetical Solution

Determine the design peak runoff rate using the rational method for a 10-year return period storm from a 120-acre suburban/agricultural watershed near Moweaqua, IL, with the following characteristics:

| Area (acres) | Percent Slope | Soil Group | Description of Area |
| --- | --- | --- | --- |
| 40 | Flat 2% | B | Single Family Res. |
| 80 | 4 % | B | Cultivated Land |

The time of concentration of the watershed is 24 minutes.

| Area (acres) | % Slope | Soil Group | Description of Area | C | C x Area |
| --- | --- | --- | --- | --- | --- |
| 40 | Flat 2% | B | Single Family Res. | 0.3 | 12 |
| 80 | 4 % | B | Cultivated Land | 0.5 | 40 |
| Area weighted C = (40+12)/120 | 0.43 |

10-year return period data for Moweaqua.

| Duration | Duration | Amount | Intensity |
| --- | --- | --- | --- |
| (h) | (min) | (in) | (iph) |
| 3 | 180 | 2.85 | 0.950 |
| 2 | 120 | 2.62 | 1.310 |
| 1 | 60 | 2.09 | 2.090 |
| 0.5 | 30 | 1.64 | 3.280 |
| 0.25 | 15 | 1.2 | 4.800 |
| 0.167 | 10 | 0.98 | 5.868 |
| 0.0833 | 5 | 0.53 | 6.363 |

Interpolating between 15 and 30 minutes

Intensity for 24 minutes = 3.280 + (4.8-3.28)*(30-24)/(30-15) = 3.89 iph

Q = CIA = 0.43*3.89*120 =  200.7 cfs

Determine the peak runoff rate from an 800 ha watershed near Lawrenceville, IL experiencing a 10-year – 6 hour storm event.  The weighted curve number for the watershed is 72.  The length of flow in the watershed is 2,500 meters.  The elevation drop across the watershed is 35 meters.   Plot the hydrograph.

L = 2500 m =  8202 ft

S = 35/2500 = 0.014

Tc	= 0.00526 L0.8(1000/CN – 9)0.7 S-0.5

= 0.00526 (8202)0.8(1000/72 – 9)0.7 (0.014)-0.5

= 182.601632 minutes = 3.04 hours

Tp = D/2 + TL = D/2 + 0.6Tc   = 6/2 + 0.6*3.04 = 4.42 hours

10-year – 6 hour amount for Lawrenceville = 3.37 inches

Ia = 0.2S = 0.2 * 3.89 = 0.778

= 0.808 inches = 0.808*25.4 = 20.5 mm

q 	= 0.0021QA/Tp

= 0.0021*20.5*800/4.42

= 7.792 m3/s = 275.2 cfs