A. Drainage Example

A) The following information is available for subsurface drainage design.

Drain pipe depth = 4 ft; depth to water table midway between drains = 1.6 ft; depth to impermeable layer = 28 ft; drainage coefficient = 3/8 in/day; and hydraulic conductivity = 0.1 ft/hour

Estimate the required drain spacing. Use the attached Equivalent Depth Chart.

K = 0.1 x 24 = 2.4 ft/day

m = 4 – 1.6 = 2.4 ft

=  1769.5 + 1476.6 de

| S | de | S’ |
| --- | --- | --- |
| 120 ft | 8.5 | 119.7 |

B. Subirrigation Example

B) The following information is available for subsurface irrigation design.

Drain pipe depth = 4 ft; depth to water table midway over drains = 1.6 ft; depth to water table midway between drains = 2.5 ft; depth to impermeable layer = 28 ft; irrigation coefficient for corn = 1/4 in/day; and hydraulic conductivity = 0.1 ft/hour

Estimate the required drain spacing. Use the attached Equivalent Depth Chart.

K = 0.1 x 24 = 2.4 ft/day

m = 4 – 2.5 = 1.5 ft

y0 = 4 – 1.6 = 2.4 ft

=

C) The following information is available for subsurface irrigation design.

Drain pipe depth = 4 ft; depth to water table midway over drains = 1.6 ft; depth to water table midway between drains = 2 ft; depth to impermeable layer = 28 ft; irrigation coefficient for corn = 1/4 in/day; and hydraulic conductivity = 0.1 ft/hour

Estimate the required drain spacing. Use the attached Equivalent Depth Chart.

K = 0.1 x 24 = 2.4 ft/day

m = 4 – 2 = 2 ft

y0 = 4 – 1.6 = 2.4 ft

=