# Runoff

Runoff starts when the rainfall rate exceeds the rate of infiltration. For lumped models rainfall volume can be obtained by integrating the rainfall excess:

Where Q is the runoff volume, i is the rainfall rate, and f is the infiltration rate. Various methods have been developed to determine flow volumes, peak flow rates, and runoff hydrographs.  These methods work reasonably well for hydrologic models, but are less effective for water quality models, since sediment or chemical concentrations are dependent on flow path.

# Estimating Runoff Volume

SCS (NRCS) Curve Number Method

In this method, the total rainfall is separated into three components as shown below,

Ia is the initial abstraction before ponding (in),

P is the cumulative rainfall (in)

Q is the runoff (in)

Q is estimated from the following relationships:

Where S = maximum soil water storage potential (in) and is given by

Values of CN, the Curve Number, have been established for various situations.

Average coefficients are calculated for composite areas:

where Ci is the coefficient applicable to the area Ai.

Adjusting for Antecedent Moisture

| Rainfall Groups for Antecedent Soil Moisture Conditions during Growing and Dormant Seasons |
| --- |
| Antecedent Condition | Description | Growing Season 5-Day Antecedent Rainfall | Dormant Season 5-Day Antecedent Rainfall |
| Dry AMC I | An optimum condition of watershed soils, where soils are dry but not to the wilting point, and when satisfactory plowing or cultivation takes pace | Less than 1.4 in. or 35 mm | Less than 0.05 in. or 12 mm |
| Average AMC II | The average case for annual floods | 1.4 in. to 2 in. or 35 to 53 mm | 0.5 to 1 in. or 12 to 28 mm |
| Wet AMC III | When a heavy rainfall, or light rainfall and low temperatures, have occurred during the five days previous to a given storm | Over 2 in. or 53mm | Over 1 in. or 28 mm |

| Land Use Description on Input Screen | Curve Numbers from TR-55 (Urban Hydrology) |
| --- | --- |
|  | Cover Description | Curve Number for Hydrologic Soil Group |
|  | Cover Type and Hydrologic Condition | % Impervious Areas | A | B | C | D |
| Agricultural | Row Crops - Staight Rows + Crop Residue Cover- Good Condition (1) |  | 64 | 75 | 82 | 85 |
| Commercial | Urban Districts: Commerical and Business | 85 | 89 | 92 | 94 | 95 |
| Forest | Woods(2) - Good Condition |  | 30 | 55 | 70 | 77 |
| Grass/Pasture | Pasture, Grassland, or Range(3) - Good Condition |  | 39 | 61 | 74 | 80 |
| High Density Residential | Residential districts by average lot size: 1/8 acre or less | 65 | 77 | 85 | 90 | 92 |
| Industrial | Urban district: Industrial | 72 | 81 | 88 | 91 | 93 |
| Low Density Residential | Residential districts by average lot size: 1/2 acre lot | 25 | 54 | 70 | 80 | 85 |
| Open Spaces | Open Space (lawns, parks, golf courses, cemeteries, etc.)(4) Fair Condition (grass cover 50% to 70%) |  | 49 | 69 | 79 | 84 |
| Parking and Paved Spaces | Impervious areas: Paved parking lots, roofs, drivesways, etc. (excluding right-of-way) | 100 | 98 | 98 | 98 | 98 |
| Residential 1/8 acre | Residential districts by average lot size: 1/8 acre or less | 65 | 77 | 85 | 90 | 92 |
| Residential 1/4 acre | Residential districts by average lot size: 1/4 acre | 38 | 61 | 75 | 83 | 87 |
| Residential 1/3 acre | Residential districts by average lot size: 1/3 acre | 30 | 57 | 72 | 81 | 86 |
| Residential 1/2 acre | Residential districts by average lot size: 1/2 acre | 25 | 54 | 70 | 80 | 85 |
| Residential 1 acre | Residential districts by average lot size: 1 acre | 20 | 51 | 68 | 79 | 84 |
| Residential 2 acres | Residential districts by average lot size: 2 acre | 12 | 46 | 65 | 77 | 82 |
| Water/ Wetlands |  | 0 | 0 | 0 | 0 | 0 |

| Runoff curve numbers for hydrologic soil cover | Hydrologic Soil Group |
| --- | --- |
| Land Use | Treatment or Practice | Hydrologic Condition | A | B | C | D |
| Fallow | Straight Row | --- | 77 | 86 | 91 | 94 |
| Row Crops | Straight Row | Poor | 72 | 81 | 88 | 91 |
|  |  | Good | 67 | 78 | 85 | 89 |
|  | Contoured | Poor | 70 | 79 | 84 | 88 |
|  |  | Good | 65 | 75 | 82 | 86 |
|  | Terraced | Poor | 66 | 74 | 80 | 82 |
|  |  | Good | 62 | 71 | 78 | 81 |
| Small Grain | Straight Row | Poor | 65 | 76 | 84 | 88 |
|  |  | Good | 63 | 75 | 83 | 87 |
|  | Contoured | Poor | 63 | 74 | 82 | 85 |
|  |  | Good | 61 | 73 | 81 | 84 |
|  | Terraced | Poor | 61 | 72 | 79 | 82 |
|  |  | Good | 59 | 70 | 78 | 81 |
| Close-seeded Legumes or Rotation Meadow | Straight Row | Poor | 66 | 77 | 85 | 89 |
|  |  | Good | 58 | 72 | 81 | 85 |
|  | Contoured | Poor | 64 | 75 | 83 | 85 |
|  |  | Good | 55 | 69 | 78 | 83 |
|  | Terraced | Poor | 63 | 73 | 80 | 83 |
|  |  | Good | 51 | 67 | 76 | 80 |
| Pasture or Range | Natural | Poor | 68 | 79 | 86 | 89 |
|  |  | Fair | 49 | 69 | 79 | 84 |
|  |  | Good | 39 | 61 | 74 | 80 |
|  | Contoured | Poor | 47 | 67 | 81 | 88 |
|  |  | Fair | 25 | 59 | 75 | 83 |
|  |  | Good | 6 | 35 | 70 | 79 |
| Meadow | Natural | Good | 30 | 58 | 71 | 78 |
| Woods | Natural | Poor | 45 | 66 | 77 | 83 |
|  |  | Fair | 36 | 60 | 73 | 79 |
|  |  | Good | 25 | 55 | 70 | 77 |
| Farmsteads | --- | --- | 59 | 74 | 82 | 86 |
| Roads | (dirt) | --- | 72 | 82 | 87 | 89 |
|  | (hard surface) | --- | 74 | 84 | 90 | 92 |

Definition of SCS Hydrologic Soil Groups:

3.4 Definition of SCS Hydrologic Soil Groups:

( The SCS has classified more than 4000 soils into four hydrologic soil groups (HSG) according to their minimum infiltration rate obtained for bare soil after prolonged wetting.

Soil Group		Description				      Final Infiltration		Soil

Rate (mm/h)	        Texture

A		Lowest runoff potential.  Includes deep		8-12		sand,

sands with very little silt and clay, also				loamy sand,

deep, rapidly permeable loess.					sandy loam

B		Moderately low runoff potential.  Mostly		4-8		silt loam,

sandy soils less deep than A, and loess less				loam

deep or less aggregated than A, but the group

as a whole has above-average infiltration

after thorough wetting

C		Moderately high runoff potential.  Comprises	1-4		sandy clay

shallow soils and soils containing considerable			loam

clay and colloids, though less than those of group

D.  The group has below-average infiltration after

presaturation.

D		Highest runoff potential.  Includes mostly clays of	0-1		clay loam,

high swelling percent, but the group also includes			silty clay

some shallow soils with nearly impermeable				loam,

subhorizons near the surface.						sandy clay,

silty clay,

clay

# Estimating Peak Discharge

When water entering an area is more than what can be transmitted or routed by established watercourses, flooding occurs.  Generating hydrographs from big storms becomes the job of flood prediction.  We use the word prediction because we still deal with probabilities of events.

Some of the reasons we study runoff peaks and volumes are:

To quantify the volume and rate of water to be handled by water management facilities

To predict soil erosion and transport of surface pollutants

To identify critical non-point source pollution areas

Peak Discharge –  The maximum volume flow rate passing a particular location during a storm event.  Peak discharge has units of volume/time (e.g. ft3/sec, m3/sec, acre-feet/hour).

The peak discharge is a primary design variable for the design of stormwater runoff facilities such as pipe systems, storm inlets and culverts, and small open channels.  It is also used for some hydrologic planning such as small detention facilities in urban areas.

There have been many different approaches for determining the peak runoff from an area.  As a result many different models (equations) for peak discharge estimation have been developed.

Ideally, we would like to have a 30-year flood record available at every site where a peak discharge estimate is needed for design work.  If such data were always available, then a frequency analysis of the flood record could be used to characterize the flood potential at the site of the design work.

More often than not, flood records are rarely available where peak discharge estimates are needed for design work.  Therefore, it is necessary to use either a prediction method that was developed from flood frequency analyses of gaged data in the region or an uncalibrated prediction equation that was designed for use at ungaged sites.

.

Rational Method

The most widely used uncalibrated equation is the Rational Method.  Mathematically, the rational method relates the peak discharge (q, m3/sec) to the drainage area (A, ha), the rainfall intensity (i, mm/hr), and the runoff coefficient (C).

SI Units			q = 0.0028CiA

Where  q = design peak runoff rate in m3/s

C = the runoff coefficient

i = rainfall intensity in mm/h for the design return period and for a duration equal to the “time of concentration” of the watershed.

English Units			q = CiA

Where q – ft3/sec

i = rainfall intensity (in/hr)

A = watershed area in acres

C = runoff coefficient, ratio of the peak runoff rate to the rainfall intensity, dimensionless

To use the rational method there are a few assumptions.

- Rainfall intensity and duration is uniform over the area of study

- Storm duration must be equal to or greater than the time of concentration of the watershed.

Time of Concentration (Tc)

Definition – The time required for water to flow from the most remote (in time of flow) point of the area to the outlet once the soil has become saturated and minor depressions filled.  It is assumed that when the duration of the storm equals the time of concentration, all parts of the watershed are contributing simultaneously to the discharge at the outlet.  There are several methods for computing time of concentration.  Two of the most popular methods are the Kirpich equation and the SCS lag formula.

Kirpich Formula

Tc = 0.0078 L0.77S-0.385

where	Tc  =  time of concentration in minutes.

L   =  maximum length of flow (ft)

S   =  the watershed gradient (ft/ft )or the difference in elevation between the outlet and the most remote point divided by the length L.

SCS Lag Formula

Tc = 0.00526 L0.8(1000/CN – 9)0.7 S-0.5

where L = watershed length (ft)

S = watershed slope (ft/ft)

CN = curve number

Rational Method Runoff Coefficients

The rational method uses runoff coefficients in the same fashion as the SCS curve number method for estimating runoff volume.   Below are several tables for different land conditions.

Runoff Coefficient C for Agricultural Watersheds [Soil Group B] (Schwab et al., 1993).

Crop and Hydrologic		Coefficient C for Rainfall Rates of

Condition			25 mm/h		100 mm/h		200 mm/h

Row crop, poor practice		  0.63			  0.65			   0.66

Row crop, good practice		  0.47			  0.56			   0.62

Small grain, poor practice	  	  0.38			  0.38			   0.38

Small grain, good practice	  	  0.18			  0.21			   0.22

Meadow, rotation, good		  0.29			  0.36			   0.39

Pasture, permanent, good		  0.02			  0.17			   0.23

Woodland, mature, good		  0.02			  0.10			   0.15

C Factor Conversion Factors for Hydrologic Soil Groups A, C, and D.

Crop and Hydrologic		Factors for Converting C from Group B Soils to

Condition			Group A		Group C		Group D

Row crop, poor practice		  0.89			  1.09			   1.12

Row crop, good practice		  0.86			  1.09			   1.14

Small grain, poor practice	  	  0.86			  1.11			   1.16

Small grain, good practice	  	  0.84			  1.11			   1.16

Meadow, rotation, good		  0.81			  1.13			   1.18

Pasture, permanent, good		  0.64			  1.21			   1.31

Woodland, mature, good		  0.45			  1.27			   1.40

Average coefficients are calculated for composite areas:

where Ci is the coefficient applicable to the area Ai.

SCS Triangular Hydrograph Method

In this method, peak runoff is determined using the curve number approach.  The assumption of uniform rainfall still applies.  The hydrograph takes on a triangular shape with equal peak and flow volume as in the rational method.  This can be seen below.

Peak runoff rate is calculated by

q = 0.0021QA/Tp

where	Q = runoff volume in mm depth (from the curve number)

q = runoff rate in m3/s

A = watershed area in ha.

Tp = time of peak in hours

In this method, the “time to peak” does not equal the time of concentration as in the rational method, in this method time to peak Tp equals

Tp = D/2 + TL = D/2 + 0.6Tc

Where Tp = time to peak (hours)

D  = duration of excess rainfall

TL = time of lag

Tc = time of concentration

It is assumed that the total time of flow is 2.67 Tp and the recession time of the hydrograph is 1.67 Tp.

Time of concentration is calculated using the SCS Lag formula discussed earlier