## Slide 1: Soil Erosion
Chad Lentz

## Slide 2: Why Care?
Removes valuable topsoil
Carries away expensive nutrients
Increase tillage costs to fix
Creates algae blooms and dead zones due to excess nutrients in waterways

## Slide 3: Types of Erosion
Wind:
    Problem with dry, bare land with high winds
    Not easily seen in some instances
Water:
    Problem in steep sloped areas
    Causes problems with marine life
    Has many forms that vary in severity

## Slide 4: Types of Water Erosion
Sheet Erosion
Rill Erosion
Gully Erosion
Stream bank Erosion

## Slide 5: Sheet Erosion
Soil is removed evenly
Only removes a small layer of soil from the area
Quickly turns into rill erosion

## Slide 6: Rill Erosion
Small channels of water can be seen
Soil is beginning to move away at a quicker rate
Can still be fixed with normal tillage practices

## Slide 7: Gully Erosion
Large channels that carry away soil and water
Generally removes less soil than sheet and rill erosion
Can no longer be fixed with tillage practices
If left unchecked can become a major problem

## Slide 8: Stream Bank Erosion
Constantly occurring due to constant presence of water
Can be accelerated by vegetation removal, farming to close to streambed, or straightening the channel
Soil is instantly taken away
Can cause stream to move over time

## Slide 9: Factors Affecting Erosion
Topography:
    Slope: Length and Steepness
    Shape of the watershed
Soil Texture & Structure:
    Size of soil particles:
        Sand: Easily detached, not easily moved however
        Clay: Not easily detached, but easily moved
    Infiltration Rate of Soil
    Organic Matter content & water holding capacity

## Slide 10: Factors Affecting Erosion (cont.)
Climate:
    Rainfall intensity and duration
Soil Cover
    Crops Planted
        Corn, soybeans, etc.
    Tillage practices
        No-till, conservation, conventional, etc.
    Land Management
        Contour farming, surface & subsurface drainage, etc.

## Slide 11: Erosion Control Methods
Contour Farming:
    Farming parallel to the elevation contours vs. farming up and down the slope
    Causes row crops and tillage ridges to intercept and slow down water
    Can not be done in all cases

## Slide 12: Erosion Control Methods
Tillage Management Practices
    Not using conventional tillage (plowing under all residue)
    Using conservation tillage (leaving 30% of residue) and no-till methods

## Slide 13: Tillage Management Practices

## Slide 14: Erosion Control Methods
Tile and Dry Dam Installation
    Dry dams slow water down
    Tile gets the water off the surface
    Generally improves crop yield as well
    Dry dams require maintenance over time
    https://www.youtube.com/watch?v=UxHYwrBIyZ8

## Slide 15: Tiling and Dry Dams

## Slide 16: Erosion Control Methods
Natural Vegetation Cover
    Waterways slow erosion
    Leaving forest and grass strips along gullies and streams can slow erosion and slow nutrient loss
    Roots anchor soil along streams
    Cover crops

## Slide 17: Vegetative Cover

## Slide 18: In Conclusion
Soil erosion is a major problem affecting farmers
Needs to be kept in check before it becomes a unmanageable
Many methods to control erosion that work good
https://www.youtube.com/watch?v=EzKyi4KuOEE